## Slide 1
Basic Relationship between pixels

## Slide 2: Contents
Neighborhood
Adjacency
Connectivity
Paths
Regions and boundaries

## Slide 3: Relationship between pixels

## Slide 4
Conventional indexing method
(x-1, y-1) | (x-1,y) | (x-1,y+1)
(x,y-1) | (x,y) | (x,y+1)
(x+1, y-1) | (x+1,y) | (x+1, y+1)
x
y
(0,0)

## Slide 5: Neighbors of a pixel
N4(P): 4-neighbors of p
(x-1, y-1) | (x-1,y) | (x-1,y+1)
(x,y-1) | (x,y) | (x,y+1)
(x+1, y-1) | (x+1,y) | (x+1, y+1)

## Slide 6
  : four diagonal neighbors of p
(x-1, y-1) | (x-1,y) | (x-1,y+1)
(x,y-1) | (x,y) | (x,y+1)
(x+1, y-1) | (x+1,y) | (x+1, y+1)

## Slide 7
N8(P): 8-neighbors of p
N4(P) and ND(P)
(x-1, y-1) | (x-1,y) | (x-1,y+1)
(x,y-1) | (x,y) | (x,y+1)
(x+1, y-1) | (x+1,y) | (x+1, y+1)

## Slide 8: Adjacency
V: The set of gray-level values used to define adjacency
4-adjacency: Two pixels p and q with values from V are 4-adjacent if q is in the set N4(p).
8-adjacency: Two pixels p and q with values from V are 8-adjacent if q is in the set N8(p).
V={0,1} V={1,2}
0 | 1 | 0
0 | 1 | 0
0 | 0 | 0
0 | 1 | 1
0 | 2 | 0
0 | 0 | 1

## Slide 9
m-adjacency: Two pixels p and q with values from V are m-adjacent if
(i) q is in the set N4(p), or
(ii) q is in the set ND(p) and the set N4(p) ∩ N4(p) has no pixels whose values are from V.

## Slide 10: Digital Path
A path from pixel p with coordinates (x, y) to pixel q with coordinates (s, t) is a sequence of distinct pixels with coordinates:
(x 0, y 0), (x 1, y 1), (x2, y 2) … (x n, y n), where (x 0, y 0)=(x, y) and
(x n,yn)=(s, t); (x i, y i ) is adjacent to (xi-1, yi-1)
Length of path = n
4/8/m-paths

## Slide 11: Connectivity
Connected Pixels:
If p and q are pixels of an image subset S then p is connected to q in S if there is a path from p to q consisting entirely of pixels in S
Connected component:
For every pixel p in S, the set of pixels in S that are connected to p is called a connected component of S
Connected Set:
If S has only one connected component then S is called Connected Set

## Slide 12: Region and boundary
Region: A subset R of pixels in an image is called a Region of the image if R is a connected set.
Adjacent Regions:

## Slide 13: Border and Edge
Foreground: If an image contains ‘K’ disjoint regions, Rk, k=1,2,…..N, then
Background: ()c
Border: of a region ‘R’ is the set of points that are adjacent to points in complement of ‘R’

## Slide 14
Edge: It is intensity discontinuity
Edge point
Edge segment
border

## Slide 15: Distance Measures

## Slide 16: Types

## Slide 17
D4<=2 from (x, y)
D8<=2 from (x, y)

## Slide 18: Practice Exercises
V= {2,3,5}

## Slide 19
Compute shortest 4-, 8-, m-paths between pixels p and q where
V= {1, 2}

## Slide 21
Consider the following matrix corresponding to pixel values of image.
Compute:
1) Spatial Resolution
2) Intensity resolution
3) Image contrast
4) Dynamic range
5) Gray scale